## Slide 1: ➢ Starting point: a basic U-Net
▼ Input: spectrogram, 1 × 512 × 512 (time × frequency)
Output: an RFI probability for every pixel ▲
Encoder 1 · 8 × 512 × 512
2 × (3×3 conv → ReLU)
Decoder 1 · 8 × 512 × 512
join skip → 2 × (3×3 conv → ReLU)
Encoder 2 · 16 × 256 × 256
2 × (3×3 conv → ReLU)
Decoder 2 · 16 × 256 × 256
join skip → 2 × (3×3 conv → ReLU)
Encoder 3 · 32 × 128 × 128
2 × (3×3 conv → ReLU)
Decoder 3 · 32 × 128 × 128
join skip → 2 × (3×3 conv → ReLU)
Encoder 4 · 64 × 64 × 64
2 × (3×3 conv → ReLU)
Decoder 4 · 64 × 64 × 64
join skip → 2 × (3×3 conv → ReLU)
skip connection: copy the encoder's features and join them to the decoder's
max-pool: half size
up-conv: double size
max-pool: half size
up-conv: double size
max-pool: half size
up-conv: double size
Bottleneck · 128 × 32 × 32
2 × (3×3 conv → ReLU)
Encoder (left): shrinks the image step by step and learns WHAT is in it.
Decoder (right): grows it back to full size and learns WHERE it is.
Skip connections: pass fine detail straight across, so thin RFI lines are not lost when the image is shrunk.
Numbers: channels × height × width.
Drawn at our model's sizes so slides 1 and 2 line up box for box. Akeret's tf_unet (our baseline) is this design, but shrinks only twice (32 → 64 → 128 channels, 465,986 parameters) and trims the border, so 512 × 512 in gives 472 × 472 out.

## Slide 2: ➢ Our model: the same U, changed inside
▼ Input: spectrogram, 1 × 512 × 512 — no border trimming ⑦
1×1 conv → 2 raw scores → softmax ⑤ → RFI probability ▲
Encoder 1 · 8 × 512 × 512
ResBlock ②④ → Strip ① → ECA ③
Decoder 1 · 8 × 512 × 512
join skip → ResBlock ②④ → ECA ③
Encoder 2 · 16 × 256 × 256
ResBlock ②④ → Strip ① → ECA ③
Decoder 2 · 16 × 256 × 256
join skip → ResBlock ②④ → ECA ③
Encoder 3 · 32 × 128 × 128
ResBlock ②④ → Strip ① → ECA ③
Decoder 3 · 32 × 128 × 128
join skip → ResBlock ②④ → ECA ③
Encoder 4 · 64 × 64 × 64
ResBlock ②④ → ECA ③
Decoder 4 · 64 × 64 × 64
join skip → ResBlock ②④ → ECA ③
skip connection: copy the encoder's features and join them to the decoder's
max-pool: half size
up-conv: double size
max-pool: half size
up-conv: double size
max-pool: half size
up-conv: double size
Bottleneck · 128 × 32 × 32
ResBlock ②④ → Strip ①
① Strip convolutions — 7/11/21-px windows (enc. 1–3, bottleneck)
② Residual shortcut — inside every ResBlock
③ ECA attention — after every encoder and decoder block
④ GroupNorm — in every ResBlock and strip (tf_unet: none)
⑤ Raw scores — no ReLU before softmax (tf_unet has one)
⑥ Dice + cross-entropy loss (tf_unet: cross-entropy only)
⑦ Same padding — every pixel gets a prediction
⑧ No class weighting — tf_unet has none either; our earlier version used it and scored lower
⑨ Size: shrinks 4 times, 8 → 128 channels, 593,842 parameters
Red = the three added modules ①–③

## Slide 3: ➢ Inside one level, step by step
ResBlock ②④
Two 3×3 convolutions, each tidied by GroupNorm; the input is added back at the end. Dropout works in training only.
Strip module ①
Looks at wider areas (7, 11, 21 px) cheaply: a thin filter along frequency, then one along time.
ECA attention ③
Gives each feature map a weight between 0 and 1, then scales it.
input
3×3 conv
GroupNorm ④
ReLU
Dropout
3×3 conv
GroupNorm ④
+
ReLU
output
1×1 conv
② shortcut: input goes around the block and is added back (via a 1×1 conv: every ResBlock here changes the channel count)
input
copy (unchanged)
1×7 → 7×1
1×11 → 11×1
1×21 → 21×1
join all 4
(concatenate)
1×1 conv (mix)
GroupNorm ④
ReLU
output
Each path = 1×K along frequency, then K×1 along time, each channel on its own → together it covers a K×K square (measured)
input
average each feature map → 1 number
1-D conv (k = 3) across neighbouring channels
sigmoid → weight 0 to 1
×
output
the feature maps themselves go straight to × and are scaled by their weights

## Slide 4: ➢ From output to RFI mask, and how it learns
Using the model
after training
spectrogram
scale to 0–1 (fixed range)
Our model
probability 0–1 for each pixel
threshold (picked on validation images)
RFI mask: yes / no per pixel
Training
28,000 steps, one image per step
model's probabilities
AOFlagger's RFI mask
loss = cross-entropy + Dice ⑥
how wrong the model is; no class weighting ⑧
Adam optimiser
nudges all 593,842 numbers to lower the loss
Every 1,400 steps
check on 150 validation images; keep the best version
How it is scored: 109 test images labelled by a human expert; F1 at the best threshold (the standard for this benchmark); 3 runs each, mean ± spread.
Our model 0.6603 ± 0.0040 vs Akeret's tf_unet 0.5482 ± 0.0139 → about +0.11.
Which parts matter? Removing ①②③ gives 0.6585 — not significant (p = 0.64). Removing ④ as well gives 0.6495 — also not significant (p = 0.48).
So the gain over tf_unet sits mainly in ⑤ ⑥ ⑦ ⑨ (raw output, Dice loss, same padding, size and training setup) — not yet tested one at a time.